## Slide 1: 자동 채점 및 평가 시스템 Selective repeat
Mir-Lab, Hanyang University
Version | Date | Writer | Modification | Note
1.0 | 2018-08-07 | GILHO LEE | Selective repeat | -

## Slide 2: Outline
ARQ – Selective repeat
  Explanation (Development Environment, Testing Factors)
  System Architecture
  Flowchart
  Scoring table design
  Code Explanation
  How to execute (Screenshot)
  Future Work

## Slide 3: Selective repeat
Go-Back-N is NOT suitable for ‘noisy links’ –
in case of a lost/damaged frame a whole window of frames
need to be resent
              excessive retransmissions use up the
bandwidth and slow down transmission
Selective Repeat ARQ overcomes the limitations
of Go-Back-N by adding 2 new features
receiver window > 1 frame, so that out-of-order but error-free frames can be accepted
retransmission mechanism is modified – only individual frames are retransmitted
Selective Repeat ARQ is used in TCP

## Slide 4: 1) Explanation
Development Environments
Language
Complier version : Java 1.8u version
Server Library : java.sun.HTTP Server
WEB Page : CSS, HTML
Database : MySQL

## Slide 5: 1) Explanation
Testing Factors
채점항목 | Data | Suc or fail
Data | Hi | success
Data가 제대로 도착했는가 |  | 
Time check | 5sec | success
정해놓은 범위를 초과했는가 |  | 
재전송 여부 | Ok | success
NAK를 받은 프레임의 재전송 했는가 |  | 
다시 순차적 전송 | Ok | success
이전에 진행했던 번호 다음부터 전송했는가 |  | 
Window size | 5 | success
정해진 크기만큼 도착했는가 |  | 
ACK check (1~n) | From n | success
ACK가 1번부터 N번까지 왔는가 |  | 
UDP Server Multi Thread Check | ok | success
Client 의 프로그램이 multi Thread로 구현되어있는지 |  | 
P2P Structure Check | ok | success
Client 의 프로그램이 p2p Structure 로 구현되어있는지 |  | 

## Slide 6: 4) Scoring table design
rcv ack1, send pkt2
채점항목 | Data | Suc or fail
Data | Hi | success
Data가 제대로 도착했는가 |  | 
Time check | 5sec | success
정해놓은 범위를 초과했는가 |  | 
재전송 여부 | Ok | success
NAK를 받은 프레임의 재전송 했는가 |  | 
다시 순차적 전송 | Ok | success
이전에 진행했던 번호 다음부터 전송했는가 |  | 
Window size | 5 | success
정해진 크기만큼 도착했는가 |  | 
ACK check (1~n) | From n | success
ACK가 1번부터 N번까지 왔는가 |  | 
UDP Server Multi Thread Check | ok | success
Client 의 프로그램이 multi Thread로 구현되어있는지 |  | 
P2P Structure Check | ok | success
Client 의 프로그램이 p2p Structure 로 구현되어있는지 |  | 
sender
receiver
send pkt0
send pkt1
send pkt2
send pkt3
Receive pkt0, send ack0
Receive pkt1, send ack1
Receive pkt3, buffer,
send ack3
rcv ack0, send pkt4
rcv ack3, send pkt5
Receive pkt4, buffer,
send ack4
rcv ack4
loss
Receive pkt2, buffer,
send ack2
rcv ack2
Pkt2 timeout
rcv ack5
Receive pkt5, buffer,
send ack5
Notes: 실패한 프레임에 대한 올바른 처리 체크

## Slide 7: 2) System Architecture
Database
Shared Memory
Main
HTTP Server
Sub
HTTP Server
(각 학생에게 할당)
Create Socket
Data Store
Data Query
채점 내용 저장
채점 내용 저장
166.104.143.225:9998/index.html
166.104.143.225:(Random)/test/index
MySQL
166.104.143.225:3306

## Slide 8: 3) Flowchart – (5)
Send window size number
Client
Main Thread
Save data from server
DB
if successful about connect to client
between server, send test page.
Click the run button
Send window size input page
Set window size number in code
and check connect to client and server
Send first frame
Receive ack Send last(win size) frame
Send ack about receive frame
Send ack about receive last frame
Receive ack Send first(last+1) frame
Send ack about receive frame
Send nak about receive frame
Receive ack Send last(win size*2) frame
Receive ack Send frame about nak
Send ack about receive last frame
Send ack about receive frame(nak)
Receive ack Send first(win size*2+1)frame
Receive ack Send last frame
receive frame and send info to db
Include timeout check
Notes: 연결을 하고 나서
실행버튼을 통해 미리 설정되어있는 데이터를 서버로 보낸다.
고의적으로 NAK를 보내 프로그램의 완성도 체크가능

## Slide 9: 3) Flowchart – (1)
시작
Create Management Thread
Main Thread
Management Thread
Get Expired Data from DB
DB
3 minute
Delete Expired Files
Sleep few second
Create Server Socket for main page
A
Notes: Get Expired Data from DB (example query)
select html_file, image_file1, image_file2, image_file3 from client_test where timestamp < DATE_ADD(now(), INTERVAL -3 minute)

## Slide 10: 3) Flowchart – (2)
Create Sub thread
for processing request
Main Thread
Sub Thread #1
Send User Data
Client #1
Client #2
(for test)
A
DB
Sub Thread #2
Exit thread
Send main page
Create Sub thread
for processing request
Connect to main page
Exit thread
Send announce page
Create Random Files
Save Data to DB (random files, user data, ...)
Create Sub thread
for client test
C
D
E
F
Include test page URL
Notes: Get Expired Data from DB (example query)
select html_file, image_file1, image_file2, image_file3 from client_test where timestamp < DATE_ADD(now(), INTERVAL -3 minute)
Create Random Files
테스트용 이미지 파일 중 몇 개를 선정하여 각 파일을 무작위 이름의 파일로 복사한다.
추가로, 랜덤으로 생성된 이미지 파일의 경로를 포함하는 html 파일을 생성하여 저장한다.
바뀔수

## Slide 11: 3) Flowchart – (3)
Client #2
(for test)
DB
Sub Thread #2
Send html file
Connect to test page
D
F
Get html file
Check http header
Save result of header checking
Send image file
Connect to test page
Get image file #n
Check http header
Save result of header checking
Notes: 바뀔수가없다

## Slide 12: 3) Flowchart – (4)
Create Sub thread
for processing request
Main Thread
Sub Thread #1
Client #1
DB
Get Data from DB
Connect to answer page
C
E
Exit thread
Send answer page
Create Sub thread
for processing request
Get Data from DB
Send answer
Exit thread
Send result page
Write Result Data to DB

## Slide 13: 5) Code explain
미정

## Slide 14: 6) Future work
미정